## Slide 1: Fire tests of heating appliances fired by solid fuel
Preliminary results
PG meeting 12.10.2011
<number>
Matti J. Virtanen

## Slide 2: Finnish letter to the Commission (25.5.2011)
A lot of fire cases related to fireplaces and chimneys including also products with CE-marking
We have studied EN-standards of chimneys and fireplaces
  A lot of deficiencies
  CEN TC 295 Residential solid fuel burning appliances and CEN TC 166 Chimneys do not discussed with each others
  There are Finnish tests which gave results that EN-standards are not sufficient
Finland is the coldest country in the EU. Heating is needed.
<number>
Matti J. Virtanen

## Slide 3: Test program
We wanted to give evidences to support our requirements
Ministry of the Environment has ordered the following tests from VTT which is a notified body under the CPD
  Slow heat release fire appliances according to EN 15250
  Sauna stoves according to EN 15821
  Roomheaters fired by solid fuel according to EN 13240
  There will be a test report in English before the end of 2011
  This test program covers aspects related to fireplaces mentioned in our letter
<number>
Matti J. Virtanen

## Slide 4: First test
Test product = a commercial slow heat release appliance fired by solid fuel
Test according to EN 15250 Slow heat release appliances fired by solid fuel:Requirements and test methods
Firstly , normal test= to determine flue gas temperature in CE-marking as required in EN 15250
Next test is the safety test but flue gas temperature has also been measured (not required in EN 15250)
Finally an additional heating test (not in EN 15250)
Flue draught (red line)
<number>
Matti J. Virtanen

## Slide 5
Matti J. Virtanen
<number>

## Slide 6: Bypass device is open
Test product = the same slow heat release appliance
According to EN 15250
Bypass device is open
Bypass device is to improve ignition
Bypas device can be used in summertime avoiding heating
<number>
Matti J. Virtanen

## Slide 7
Matti J. Virtanen
<number>

## Slide 8: Sauna stove
Test sauna stove = a commercial product on the market
Test according to 15821
  Temperature is 90 oC in sauna
Next test will be the safety test according to EN 15821 where temperature of flue gas is also measured (not required in EN 15821)
<number>
Matti J. Virtanen

## Slide 9
<number>
Matti J. Virtanen

## Slide 10: What to do?
Flue gas temperature is for energy efficiency, not to determine fireclass of chimneys
There is a need to determine correct flue gas temperature for chimneys
CEN consultant has sent our letter to CEN TC 295 and TC 166.
CEN TC 295 has refused to improve its standards
What to do?
  To withdraw these standards from the OJ.
  To allow that Finland can demand an additional test in order to determine the correct flue gas temperature class of chimneys
  Something else
Matti J. Virtanen
<number>

## Slide 11: What to do with chimneys standards
CEN TC 166 has started to discuss
Deficiencies:
  Higher flue gas temperature class than T 600?
  Durability of thermal insulation material at high temperature (e.g. 500-600 oC) for longer periods
  Wall thickness of metal flue liners in CE-marking
  Thick thermal insulation in the roof
    Temperarure will much higher than tests where thermal insulation (200 mm) is used
  How to seal chimneys and how to test seals
    In the room
    On the roof
  Connection between CE-marking and assembly instructions
    There are national assembly standards and additional assembly tests in some Member States
  Reduction of tests
    E.g. One chimney type has 14 different markings
    Calculation methods should be developed
  etc
Matti J. Virtanen
<number>