## Slide 1: « Regulation 305/2011/EU: Construction Products Regulation (CPR)»
« From the problems of the CPD to the objectives of the CPR »
Vicente Leoz Argüelles
Notes: <number>

## Slide 2: From the problems of the Directive to the objectives of the Regulation: Essential elements
1. Elements of conceptual CLARIFICATION
The fact of replacing the Directive by a REGULATION
The Regulation highlights more clearly than the Directive the main differences with the « New Approach »:
 Basic Requirements of Works (instead of Essential Requirements)
 Essential Product Caracteristics (new concept).
The DoP (Declaration of Performance) is the key-concept of the CPR system.
The CE marking has a clear meaning, very different from the meaning of this term under the « New Approach ».
Notes: <number>

## Slide 3: 2. Elements of functional CLARIFICATION (rights and obligations)
The Basic Requirements of Works (Annex I) do not create « per se » any legal obligation for anyone.
The DoP is mandatory for every construction product which is covered by a harmonised standard or conforms to a European Technical Assessment (Art.4).
The DoP shall contain information about the use of the product foreseen by the manufacturer (Art.6).
It shall also contain the list of the essential characteristics which are considered pertinent in the relevant harmonised technical specification, for the declared intended use or uses .
It shall also contain the performance of at least one of the essential characteristics of the construction product in that list (NPD for others).
The CE marking is mandatory if a DoP has been drawn up(Art. 8).
The CE marking is the only marking associated with the essential characteristics of the products. No other mark, notably national marks, can make reference to them.
The CE marking shall be followed by the declared level or class of the performance (Art. 9(2)).
Notes: <number>

## Slide 4: Thank you for your attention
http://ec.europa.eu/enterprise/construction/index_en.htm
Notes: <number>