## Slide 1: Construction Products Regulation Rights and obligations of manufacturers
Pascal Bar & Gildas Guillevic
<number>
1st SCC meeting on 5th July 2011
Notes: CEPMC General Assembly
<number>

## Slide 2: CPR: Obligations for manufacturers
Provide a clear, complete and reliable information on products placed on the market
  Same obligation for all manufacturers (& importers) in Europe
Declaration of performance (DoP) for a product covered by an hEN or an ETA
  Determination of the “product-type”
    Assessment of the product performances in relation to the essential characteristics relevant for the intended use (Recital 28, Articles 4, 11)
      With the use of European methods and involvement of a Notified Body for systems 1+, 1, 2+ et 3 (Annex V)
    Implementation of a FPC in any case, complying with the requirements detailed in hEN/ETA (Annex V)
      Verification of constancy of performances, involving a Notified Body for systems 1+, 1, 2+ (Annex V)
  Drawn up a DoP
    Performances by levels or classes, for each essential characteristic listed in hEN/ETA and relevant for the declared intended use (Art 6.3)
    NPD option for characteristics not subject of any regulatory requirement where the product is used, but no empty DoP (Art 6.3)
    Reference of the product-type, system of verification of constancy of performance and ref. of hEN/ETA/STD
    Unique identification code for the DoP (Traceability)
    Information on hazardous substances provided together with the DoP (Art 6.5)
  Supply the DoP
    With each product made available on the market (Art 7.1)
    Either in paper form or by electronic means (Art 7.1), or using website under conditions to be determined by a delegated act (Art 7.3)
<number>

## Slide 3: CPR: Obligations for manufacturers
<number>

## Slide 4: CPR: Rights for manufacturers
Declaration of Performance (DoP)
  Possible derogations: Products individually manufactured or custom-made in a non-series process (Art 5.1), on the construction site (art 5.2), in a traditional manner (Art 5.3)
  Use NPD option (no test!) if the product is not regulated where the product is intended to be used
  Draw up the DoP on the basis of certificate (or declaration) of conformity (existing CE marking affixed under CPD), for products placed on the market before 01/07/2013 (Art 66.2)
Determination of Product-type: Simplified procedures
  Deemed to satisfy procedure to declare level a class (Art 27.5)
  Simplified procedures avoiding useless tests: WT/WFT, Shared IT, Cascading (Art 36)
  Specific procedures possibly used by micro-enterprises turning system 3 into system 4 (Rec 27, Art 37)
  Products individually manufactured turning system 3 into system 4 (Art 38)
European Technical Assessment
  Request an ETA when hENs do not allow to assess the product to have the benefit of CE marking (Art 19)
  Renew ETAs already delivered at the end of their validity period, and on the basis of EADs consistent with the current ETAGs or CUAPS (Recital 21, Art 66.3-4)
Information
  Product Contact Points: Inform on the existing regulatory provisions, free of charge (Rec 42-44, Art 10)
  Information campaigns for the construction sector, e.g. economic operators and users of products (Rec 54)
<number>